## Slide 1: UAV Photogrammetric Thermography for Building Performance: A Prototype
UCF / IST / IDS6938 : Building Performance Simulation

## Slide 2: Project Overview
Photogrammetry
Infrared

## Slide 3: Why?
Buildings (+ manufacturing for construction) accounts for at least 50% of energy use in the world

## Slide 4: Why IR?
Why Not?
300nm – 700nm

## Slide 5: Monitoring / Maintenance

## Slide 6: Project Overview
Photogrammetry of buildings, visible and IR energy
Use drones to carry cameras and capture video from pre-programmed flight path around buildings/sites
Capture both visible (RGB) video and IR video
Strip and post-process select frames from videos
Stitch frames with modern photogrammetry software to create 3D models
Inspect, cleanup, analyze resulting 3D models

## Slide 7: Team
Keith R. MacArthur
Joseph Del Rocco
Modeling & Simulation, Ph.D. Student
University of Central Florida
Institute for Simulation & Training
MIT2 Laboratory
keith.macarthur@knights.ucf.edu
Computer Science, Ph.D. Student
University of Central Florida
Full Sail University
joe.delrocco.org
Joseph Kider
Assistant Professor
Institute for Simulation & Training
University of Central Florida
josephkider.com
(our advisor)

## Slide 8: Prior Work 3D reconstruction of a house using a drone [9]
http://gaetanlaure.com/3d-reconstruction-of-a-house
https://skfb.ly/UFnr

## Slide 9: Prior Work The use of Unmanned Aerial Vehicles in Building Inspection [1]
Mohamed Hafez, 2015
https://www.youtube.com/watch?v=__rvoMPTc30
https://www.linkedin.com/in/mohamed-hafez-7b3b8796
[1]
Parrot AR Drone

## Slide 10: Prior Work The use of Unmanned Aerial Vehicles in Building Inspection [1]
“Designed and built a drone to be used in a unique aerial inspection of buildings and refineries.
Thermal data is captured using the drone to produce a thermal 3D mesh.
Developed a unique post-analyses method to detect thermal leaks, gas leaks, damp, and water ingress.
Project has received interest from various engineering companies including Atkins, Costain, and ExxonMobile” [1]

## Slide 11: Prior Work Visible and TIR SfM photogrammetry for temperature and heat flux [2]
FLIR T650sc
traveled on foot
102 RGB photos
2 TIR videos
[2]
[2]
[2]
[2]

## Slide 12: Prior Work Visible and TIR SfM photogrammetry for temperature and heat flux [2]
[2]

## Slide 13: Prior Work Done-based Thermal Modeling [3]
https://www.youtube.com/watch?v=x-jp9a1bpVU
Analyst Group
Pix4DM
“Overlay of thermographic (radiometric) and RGB 3D meshes of an urban area in Italy, captured with FLIR Tau 2 sensor by Analist Group, processed with Pix4Dmapper.” [3]
DJI Matrice 100 + Zenmuse X3, XT

## Slide 14: Prior Work HeatWave: A handheld 3D thermography system [6]
“The output of HeatWave is a single complete 3D multispectral model with high accuracy, view independent augmented temperature and visible information to detect any appearance, shape, temperature or temporal changes within the environment. The dense, high-resolution 3D multispectral model can be visualized in either modality independently or both simultaneously using “Spectra” the world’s first 3D multispectral visualization toolbox developed by HeatWave’s team at Autonomous Systems..” [6]

## Slide 15: Prior Work Low Cost Thermal Imaging System (for drones) [7]
Low Cost Thermal Imaging System
Advanced Control and Intelligent Systems Laboratory (ACIS)
University of British Colombia
http://acis.ok.ubc.ca/?page_id=1165
“ACIS is currently developing a lightweight low cost thermal imaging system for Unmanned Aerial Vehicles (UAVs). Applications for thermal cameras onboard UAVs include Search & Rescue and forest fire monitoring.” [7]

## Slide 16: Expected Outcomes (prototype)
A working pipeline for photogrammetry with drones
  hardware: drone, cameras, control, etc.
  software: controlling, recording, stitching, viewing, etc.
  process: setup, calibration, testing, scaling, workflow
3D models, both visible and thermal
An impressive enough prototype to warrant a professional experiment
Possibly acquire some useful analysis with models (?)

## Slide 17: General Attack Plan
Acquire + configure drones with RGB cameras
Test RGB video capture of small object (car, etc.)
Process video
    Use/write code to strip subset of frames from video
    Identify any post-processing needed
Push frames to photogrammetry software for 3D model
    Use off-the-shelf software
    Use service/API if possible
View 3D model in off-the-shelf modeling software
    Post process if necessary
Acquire + configure IR camera
    Wire camera
    Test read IR data
    Attach camera to drone
Repeat experiment of small object w/ both cameras attached
    Confirm everything is working as expected before moving on to a building/site
    Attempt experiment with residential property
Smooth any pre/post processing steps
Try a UCF / IST building
    Get permission first
    Make sure Joe is around
Collect all measurements, present results in paper and pres.

## Slide 18: Checkpoint Goals
Visible energy to 3D geometry (standard photogrammetry):
  Captured useable RGB video from drone (small object)
  Stripped/processed select frames from RGB video
  3D model from frames + photogrammetry software
IR energy to 3D geometry:
  Captured useable IR video from drone (small object)
  Stripped/processed select frames from IR video
  3D model from frames + photogrammetry software
Real experiment with building
Paper and presentation

## Slide 19: Equipment: Drones
DJI Phantom 2 Vision+
Flight time: 25m
Payload: 300g
Frequency: 5.85Ghz
Parrot AR.Drone 2.0
Flight time: 12m
Payload: 100g
Frequency: 2.4Ghz
[8]
[8]

## Slide 20: Equipment: Visible (RGB) Cameras
DIJ Phantom 2 Vision+ camera
  1920 × 1080 30p
  110°/85° hfov, 140mm f/2.8, ISO 100
Parrot AR.Drone 2.0 Canon EOS 7D
  1280 × 720 30p
  92° hfov, 38mm f/5.6, ISO 160
Tiffen Circular Polarizer Filter
  30mm
  “Filter can be rotated to achieve desired effect” (?)

## Slide 21: Equipment: IR (thermal) Camera
FLiR Lepton LWIR Imager (on breakout board)
  80 × 60 active pixels
  51° hfov, 63.5° diagonal
  Wavelengths 8 to 14 μm
  Thermal sensitivity <50 mK

## Slide 22: Equipment: IR Controller
Raspberry Pi 2 Model B v1.1 (2014)
  Broadcom BCM2836 ARMv7 Cortex-A7 4core 900MHz
  512MB RAM
  Micro SD card
  40pin GPIO
  4 USB ports
  CSI camera port
  DSI display port
  HDMI
  Micro USB power

## Slide 23: Equipment: Power Source (1)
Shenzhen PKCELL LP803860 battery (x2)
  Lithium ion polymer (LiPo)
  3.7v (4.2v max charge)
  2000mAh
  USB charger (100-500mA)
UBEC DC/DC 5v Step-Down (Buck) Converter
  Raspberry Pi needs 5v to support perhiperals

## Slide 24: Equipment: Power Source (2)
http://andicelabs.com/shop/andicelabs/power-pi/

## Slide 25: Equipment: Payload Estimate
equipment | weight
RPi controller | 40g
LiPo battery | 48g x2 = 96g
UBEC step-down converter | < 10g
IR camera + board | < 10g
switch + wires | < 15g
total weight | < 170g

## Slide 26: Equipment: Software
Drone Control:
    DJI controller + DJI Vision iOS app for Phantom 2 Vision+
    UgCS Ground Station for both Phantom or Parrot
IR Camera Controller:
    Fedora Linux + Raspberry PI API
    FLiR Lepton sample source (C/C++) + Netpbm lib
Video Frame Processing:
    Python + ffmpy (ffmpeg)
Photogrammetry:
    Autodesk Remake
    Agisoft PhotoScan Pro
    3DF Zephyr Pro

## Slide 27: Final Rig (mockup)

## Slide 28: The Therminator ™

## Slide 29: Method: Polarizing Lens (30mm)

## Slide 30: Method: IR Capture

## Slide 31: Method: Drone Flying

## Slide 32: Method: Captures

## Slide 33: Method: Resolution Experiment
1024 x 576
1920 x 1080
diff
Downscale a high res photo to equivalent resolution of IR camera
Upscale it back to original resolution
Measure loss of accuracy
Intensity map shows amount difference per pixel
Loss of accuracy is comparable at various resolutions, indicating that we don’t have to upscale IR photos to highest resolution.

## Slide 34: Method: Resolution Experiment
https://rosettacode.org/wiki/Percentage_difference_between_images#Python

## Slide 35: Problem: 110° HFOV of Phantom 2V+
. . .

## Slide 36: Problem: 110° HFOV of Phantom 2V+

## Slide 37: Solution: Lens Correction Filter
Andrew Shears “Geography & Mapping/GIS Dude” http://andrewshears.com/2014/10/08/lens-correction-on-dji-phantom-2-vision-for-mapping

## Slide 38: Solution: Set FOV to 85°
Isotropic materials are not good candidates for photogrammetry because objects appear the same from multiple directions.

## Slide 39: Problem: Manual Control of Drone
Looking at drone alone is insufficient
  Cannot ensure object is centered in view
Looking at mobile device camera feed is insufficient
  Cannot see objects near drone
Flying drone manually is ok, but not ideal
  Object will likely not be centered
  Manually navigating obstacles is stressful and dangerous
Solution: Use waypoint control software!

## Slide 40: Solution: Waypoint Software
DJI Ground Station
UgCS Ground Control

## Slide 41: Results: 3D Model from Visible

## Slide 42: Results: 3D Model from Visible

## Slide 43: Results: 3D Model from Visible

## Slide 44: Results: 3D Model from Visible

## Slide 45: Results: 3D Model from Visible

## Slide 46: Results: 3D Model from IR
visible
IR

## Slide 47: Beyond Prototype (Future Work)
More formal experiment with better infrastructure
  stronger, longer flight-time drone
  better resolution cameras
  more professional photogrammetry processing(?)
Full buildings, alternative sites, etc.
Capture more information with same pipeline (multispectral)
Studies
    downscaling/upscaling affect on photogrammetry
  Viewer plugins for popular modeling packages
    extract/select apparent temperature from thermal 3D model

## Slide 48: How you can help us 
Help us with Orlando drone regulations: - cost per flight - cost per year - insurance policy costs - FAA approvals http://orlando-politics.com/2017/01/23/city-of-orlando-passes-ordinance-regulating-drones
We need better IR equipment!
Let us scan your building and give you data

## Slide 49: References
Hafez, M. (February 2015). Photogrammetry Using a Thermal Camera attached to a Drone. Retrieved October 14, 2016, from https://www.youtube.com/watch?v=__rvoMPTc30
Lewis, A., Hilley, G., & Lewicki, J. (2015). Integrated thermal infrared imaging and structure-from-motion photogrammetry to map apparent temperature and radiant hydrothermal heat flux at Mammoth Mountain, CA, USA. Journal of Volcanology and Geothermal Research, 303, 16-24.
Pix4D, Analyst Group. (October 2015). Pix4D - Drone-based Thermal Modeling. Retrieved October 14, 2016, from https://www.youtube.com/watch?v=x-jp9a1bpVU
Moghadam, P. (2015). 3D medical thermography device, Proc. SPIE 9485, Thermosense: Thermal Infrared Applications XXXVII, 94851J.
Vidas, S. and Moghadam, P. (2013). HeatWave: a handheld 3D thermography system for energy auditing. Energy and Buildings 66, 445–460

## Slide 50: References
https://confluence.csiro.au/display/ASL/HeatWave
Ephraim, N. (n.d). Low Cost Thermal Imaging System. University of British Colombia, ACIS. Retrieved October 17, 2016 from http://acis.ok.ubc.ca/?page_id=1165
http://drones.specout.com
Laure, G. 3D reconstruction of a house using a drone. Personal website. Retrieved November 28th, 2016 from http://gaetanlaure.com/3d-reconstruction-of-a-house